## Slide 1: Lecture #7: Coding algorithms

## Slide 4: Shannon-Fano-Elias Coding
Cumulative distribution function (CDF)
Example
Chart: 
| 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5
 | 0 | 0.25 | 0.25 | 0.5 | 0.5 | 0.7 | 0.7 | 0.85 | 0.85 | 1

## Slide 5: Shannon-Fano-Elias Coding
Modified cumulative distribution function
Example

## Slide 6: Shannon-Fano-Elias Coding: An Example
Consider a random variable X taking values in the set X ={1, 2, 3, 4, 5} with probabilities 0.25, 0.25, 0.2, 0.15, 0.15, respectively.
  Using Shannon-Fano-Elias Coding method

## Slide 7: Shannon-Fano-Elias Coding: An Example
 |  |  |  | in binary |  | Codeword
1 | 0.25 | 0.25 | 0.125 | 0.001 | 3 | 001
2 | 0.25 | 0.5 | 0.375 | 0.011 | 3 | 011
3 | 0.2 | 0.7 | 0.6 | 0.10011……. | 4 | 1001
4 | 0.15 | 0.85 | 0.775 | 0.1100011…… | 4 | 1100
5 | 0.15 | 1 | 0.925 | 0.1110110…… | 4 | 1110
 |  |  |  |  |  | Codeword
1 | 0.25 | 0.25 | 0.125 | 0.001 | 3 | 001
2 | 0.25 | 0.5 | 0.375 | 0.011 | 3 | 011
3 | 0.2 | 0.7 | 0.6 | 0.10011……. | 4 | 1001
4 | 0.15 | 0.85 | 0.775 | 0.1100011…… | 4 | 1100
5 | 0.15 | 1 | 0.925 | 0.1110110…… | 4 | 1110

## Slide 8: Generic Communication System
Transmitter
Noisy Channel
Receiver

## Slide 9: Generic Communication System
Source
Encoder
Decoder
Channel
P(Y|X)
Destination
Source
Coder
Channel
Coder
Channel
Decoder
Source
Decoder
Remove Redundancy
Controlled Addition of Redundancy
Detect/Correct Errors
Restore Source

## Slide 10: Examples of Channel Capacity
EXAMPLES OF CHANNEL CAPACITY are:
  Noiseless Binary Channel
  Noisy Channel with Non overlapping Outputs
  Noisy Typewriter
  Binary Symmetric Channel (BSC)
  Z-Channel
  Binary Erasure Channel

## Slide 11: An explanation example
Random Variable (X) | Probability (pi ) | Code 1 (fixed length) | Code 2 (Variable length)
1 | 1/2 | 00 | 0
2 | 1/4 | 01 | 10
3 | 1/8 | 10 | 110
4 | 1/8 | 11 | 111
Average code length  |  | 2 | 1.75

## Slide 12: Source coding
What is source coding?
  it the process of encoding data using fewer bits than the original representation, by identifying statistical redundancy.
What is a source code?
  A source code C for a random variable X is a mapping from the range of X to a set of finite-length strings of symbols from a D -ary alphabet. Let C(x)denote the codeword corresponding to x and let l(x) denote the length of C(x).
For example, C(red) = 00, C(blue ) = 11 is a source code for X ={red, blue } with alphabet D ={0, 1}.